## Slide 1: Assessing the Impact of Transportation Electrification on the Electric Grid
Malini Ghosal*, Samrat Acharya*, Travis B Thurber,
Allison M Campbell, Casey Burleyson and Yang Ou
*Power Systems Research Engineer
Notes: Stock Image

## Slide 2: Electric Vehicle Growth
Source: *Global EV Outlook 2022, IEA
Available at: https://iea.blob.core.windows.net/
Fig: Global electric car sales, 2010-2021*
Fig: Global electric buses and trucks sales, 2015-2021*
EV market shares in 2021: Light Duty Vehicles (LDVs) – 9%, Medium Duty vehicles (MDVs) (buses, delivery vans) – 4%, Heavy Duty Vehicles (HDVs) ( heavy trucks) – 0.1%
Vehicle market share in US: LDVs -- 54.2%, MHDVs – 27.1 %**
Source: **Use of energy explained, Energy use for transportation
Available at: https://www.eia.gov/energyexplained/use-of-energy/transportation.php

## Slide 3: Growth of Electric Vehicle Charging Stations
<3 kW AC (L1)
<20 kW AC (L2)
DC Chargers: Anything above L2 (L3)
Now available 25 kW -350 kW
400 miles in single charge
>100 kWh battery
Extreme Fast Chargers (xFC)
(500kW – 4 MW)
Fig: Global LDV public chargers, 2015-2021*
Source: **Tesla Superchargers
Available at: https://www.tesla.com/supercharger
Fig: Tesla chargers**
Bipartisan Infrastructure Law building 500,000 chargers in US ( in next 5 years)
Requires changers to be 150 kW and above
Source: *Global EV Outlook 2022, IEA
Available at: https://iea.blob.core.windows.net/

## Slide 4: Electrical Grid

## Slide 5: The North American Electric Power Grid
The biggest machine!
Regions of the North American Electric
Reliability Corporation (NERC)
Notes: NAEPG is a

## Slide 6: Assessing the impact of transportation electrification
Transmission system level.
Distribution system level (not covered here).
It is important to know, when and where charging is taking place.
Therefore, generating electric load shapes from transportation sector for future year is of importance.

## Slide 7: GODEEEP: Assess transportation electric load’s impact on transmission grid operation
Assess various decarbonization scenarios- 2025-2050 in the WECC.
Downscaling transportation electric load from multi-sector dynamics model for decarbonization pathways.
Generate transportation load profile (hourly) at balancing area level.
How much does the production cost increase?
Is there enough generation?
How is the fuel mix going be impacted?
Is there transmission congestion?
  Overall Project Goal: GODEEEP addresses the resilience implications of decarbonization for United States electricity system operations and impacts on environmental and energy equity.
Goal for transportation focus sub-problem
Notes: Grid Operations, Decarbonization, Environmental and Energy Equity Platform

## Slide 8: Production cost modeling: market simulation software (GridView)
Inputs:
Hourly load profiles
Generation resources, heat rates
Transmission system topology
Output:
Generation utilization
Line utilization
Locational marginal price
Source: https://www.hitachienergy.com/

## Slide 9: Modeling transportation load for the future grid
GCAM
Multi-sector dynamics model
A coarse model giving state level yearly energy use
WRF
Meso-scale weather prediction numerical model
Transportation load down-scaling
Hourly load profile at balancing
authority level
Total Electric Load Model
Predicting the non-transportation electric load growth (climate informed)
CERF
identifies feasible, site-specific locations for individual new power plants (renewable and non-renewable)
1 km^2 spatial resolution
GridView- Production cost model
Runs unit commitment problem with future grid topology, load and generation scenario
Impact analysis
Nodal production cost
Locational marginal cost
Resource adequacy
Transmission congestion
Generation mix

## Slide 10: Transportation Load Downscaling Method

## Slide 11: Spatial Disaggregation and Fleet Size Assumption for LDV
State to county disaggregation: The county-specific LDV registration data for 2019 were used as a reference point to identify what percentage of the total number of vehicles in a state was registered in every county.
County to BA level aggregation
County level mean temperature information is used.
Fig. County level EV adoption from vehicle registration data *
[1] https://www.atlasevhub.com/materials/state-ev-registration-data#data
BA Level energy
BA Level vkm
Number of EVs in a fleet
*Kintner-Meyer, M., et al. Electric vehicles at scale–phase I analysis: High EV adoption impacts on the western US power grid. No. PNNL-29894. 2020.
Fig. Fleet Size Assumption

## Slide 12: Sample LDV Load Shape from EVI Pro*
*Wood, Eric W., et al. Charging electric vehicles in smart cities: An EVI-Pro analysis of Columbus, Ohio. No. NREL/TP-5400-70367. National Renewable Energy Lab.(NREL), Golden, CO (United States), 2018.

## Slide 13: Sample BA/County Level LDV Shape
As we can see, higher temperature during Arizona summer is impacting the battery charging/discharging model and therefore, more energy is consumed.
No assumption of month-to-month variability in total vehicles miles traveled is assumed.

## Slide 14: Transportation Load Downscaling Method

## Slide 15: MDVs & HDVs- Spatial Distribution in WECC
Cities and jurisdictions where clean air regulations (non-attainment zones) may drive zero-emission vehicle policies.
Sharing algorithm: above criteria + cities with population above 100,000.
The total number of electric MDVs was then applied based on a proportional percentage of the population of the 313 cities.
The total number of electric MDVs for the WECC are 70,000 or about 35% of the assumed national electric MDV fleet of 200,000.
Kintner-Meyer, M., et al. Electric vehicles at scale–phase I analysis: High EV adoption impacts on the western US power grid. No. PNNL-29894. 2020.

## Slide 16: Dataset Used for MDVs and HDVs
Vehicles | Classes
Delivery Vans | 3-6
Delivery Trucks | 3-7
School Buses | 3-6
Transit Buses | 7 & 8
Bucket Trucks | 3-7
Service Vans | 2 & 3
Tractors | 7 & 8
Refuse Trucks | 8
Type | Class | GVWR
LDV | 1 & 2 | <10k lbs
MDV | 3-6 | 10k-26k lbs
HDV | 7 & 8 | >26k lbs
Based on Us Federal Highway
Administration* (AFDC)
FleetDNA Commercial
Vehicles**
FleetDNA dataset for driving pattern of return-to-base commercial low-duty, medium-duty and heavy-duty vehicles is used: start time, stop time, and vehicle miles travelled.
The data is discontinuous time-series for years: 2008, 2012, 2014.
The data is anonymously collected for vehicles in US. So, no direct mapping for vehicles in WECC
The FleetDNA data is used to find distribution of start time, stop time, and vehicle miles travelled.
Used for developing charging profiles for MDVs and HDVs.

## Slide 17: MDV Load Shape Generation
Immediate
Delay
Min Power
Combined
Combined = 0.2* immediate + 0.3* delay + 0.5 min power
Low Bound Peak Demand (kW): 1444.98
Average Peak Demand (kW): 1593.67
Upper Bound Peak Demand (kW): 4871.47
Low Bound kWh/operating day: 9688.7
Average kWh/operating day: 10467.33
Upper Bound kWh/operating day: 11269.51
Low Bound Peak Demand (kW): 1171.99
Average Peak Demand (kW): 2350.86
Upper Bound Peak Demand (kW): 8082.45
Low Bound kWh/operating day: 12152.29
Average kWh/operating day: 13096.5
Upper Bound kWh/operating day: 14083.84
Low Bound Peak Demand (kW): 2225
Average Peak Demand (kW): 2143.75
Upper Bound Peak Demand (kW): 5075
Low Bound kWh/operating day: 5993.31
Average kWh/operating day: 6523.56
Upper Bound kWh/operating day: 7048.02
Low Bound Peak Demand (kW): 2250
Average Peak Demand (kW): 2005.0
Upper Bound Peak Demand (kW): 4125
Low Bound kWh/operating day: 5993.31
Average kWh/operating day: 6523.56
Upper Bound kWh/operating day: 7048.02
kw_list = [50, 125, 250, 350, 500, 1000]
kw_weights = [5, 5, 10, 40, 40, 0]
Power, KW

## Slide 18: Time-Series MDV Load in WECC
Combined = 0.2* immediate + 0.3* delay + 0.5 min power
kw_list = [50, 125, 250, 350, 500, 1000]
kw_weights = [5, 5, 10, 40, 40, 0]

## Slide 19: Conclusion
Work in progress.
The presentation outlines the methodology to accurately assess impact of transportation load on the decarbonized, future transmission grid.
Business-as-usual and net zero scenarios are assessed for a hot climate scenario.
The study will inform any resource adequacy, production cost, operational impact of rapid transportation electrification for various decarbonization scenario.
The method could be adapted for any other footprint beyond WECC.